## Slide 2
By K. L. Geijsen
Computer and Embedded Systems Engineering MSc Thesis
Why did Itanium fail
Notes: Intro

## Slide 3: Presentation structure
Introduction
Summary Itanium
Failure definition
Motivation
Experiment results
Market reception
Performance comparative analysis
Static analysis of IA-64 Binaries
Hardware complexity analysis
Differentiation business strategy framework
Conclusion
Summary
Conclusion
09-10-2020
MSc thesis: Why did Itanium fail?

## Slide 4: Summary of Itanium
Intel + HP joint project
09-10-2020

## Slide 5: Summary of Itanium
Intel + HP joint project
64-bit architecture – IA-64
27.06.2024

## Slide 6: Summary of Itanium
Intel + HP joint project
64-bit architecture – IA-64
EPIC
27.06.2024

## Slide 7: Failure definition
What were Itanium’s goals?
27.06.2024

## Slide 8: Failure definition
What were Itanium’s goals?
Performance leadership (through static ILP)
Introduce 64-bit architecture
Replace x86
27.06.2024

## Slide 9: Motivation
Such a large-scale project costing billions
Intel/HP loss, but also customers and investors
27.06.2024

## Slide 10: Motivation
Such a large-scale project costing billions
Intel/HP loss, but also customers and investors
No definitive answer yet
27.06.2024

## Slide 11: Motivation
09-10-2020
Such a large-scale project costing billions
Intel/HP loss, but also customers and investors
No definitive answer yet
Personal interest

## Slide 12: Studies performed
Public reception
Automated sentiment analysis
Technical evaluation
  SPEC performance comparative analysis
  Theoretical performance comparative analysis
  Static analysis on IA-64 binaries
  Hardware complexity comparison
Business strategy
  Differentiation strategy framework
09-10-2020
MSc thesis: Why did Itanium fail?

## Slide 13: 1. Automated sentiment analysis
Automated using Large Language Models
genai API
Sentiment
scores
27.06.2024

## Slide 14: 1. Automated sentiment analysis
Automated using Large Language Models
Results:
Public reception
27.06.2024

## Slide 15: 1. Automated sentiment analysis
Automated using Large Language Models
Results:
Public reception
Academic reception
27.06.2024

## Slide 16: 1. Automated sentiment analysis
Automated using Large Language Models
Results:
Public reception
Academic reception

## Slide 17: 1. Automated sentiment analysis
Automated using Large Language Models
Results:
Public reception
Academic reception
Conclusions:
Popularity peaks around 2004

## Slide 18: 1. Automated sentiment analysis
Automated using Large Language Models
Results:
Public reception
Academic reception
Conclusions:
Popularity peaks around 2004
Sentiment is polarized

## Slide 19: 2. SPEC performance comparative analysis
SPEC benchmarks
27.06.2024

## Slide 20: 2. SPEC performance comparative analysis
SPEC benchmarks
SPECint2000
27.06.2024

## Slide 21: 2. SPEC performance comparative analysis
SPEC benchmarks
SPECint2000
SPECfp2000
27.06.2024

## Slide 22: 2. SPEC performance comparative analysis
SPEC benchmarks
SPECint2000
SPECfp2000
SPECint2000 normalized
27.06.2024

## Slide 23: 2. SPEC performance comparative analysis
SPEC benchmarks
SPECint2000
SPECfp2000
SPECint2000 normalized
SPECfp2000 normalized
27.06.2024

## Slide 24: 2. SPEC performance comparative analysis
SPEC benchmarks
SPECint2000
SPECfp2000
SPECint2000 normalized
SPECfp2000 normalized
Conclusions
SPEC performance is competitive
27.06.2024

## Slide 25: 2. SPEC performance comparative analysis
SPEC benchmarks
SPECint2000
SPECfp2000
SPECint2000 normalized
SPECfp2000 normalized
Conclusions
SPEC performance is competitive
At normalized clock speed it performs better
27.06.2024

## Slide 26: 2. SPEC performance comparative analysis
SPEC benchmarks
SPECint2000
SPECfp2000
SPECint2000 normalized
SPECfp2000 normalized
Conclusions
SPEC performance is competitive
At normalized clock speed it performs better
Performs best in FP workloads
27.06.2024

## Slide 27: 3. Theoretical performance comparative analysis
Theoretical performance limits of EPIC
27.06.2024

## Slide 28: 3. Theoretical performance comparative analysis
Theoretical performance limits of EPIC
Speculative execution
27.06.2024

## Slide 29: 3. Theoretical performance comparative analysis
Theoretical performance limits of EPIC
Speculative execution
EPIC: Compiler chooses
Speculative?
In-order?
27.06.2024

## Slide 30: 3. Theoretical performance comparative analysis
Theoretical performance limits of EPIC
Speculative execution
EPIC: Compiler chooses
Traditional systems: Hardware chooses with Branch Predictor
27.06.2024

## Slide 31: 3. Theoretical performance comparative analysis
Theoretical performance limits of EPIC
Speculative execution
EPIC: Compiler chooses
Traditional systems: Hardware chooses with Branch Predictor
Conclusion:
EPIC will either lead to more execution overhead or latency compared to traditional systems
27.06.2024

## Slide 32: 4. Static analysis
27.06.2024

## Slide 33: 4. Static analysis
Analysis of 1,071,700 files
FTP
disassembly
analysis
27.06.2024

## Slide 34: 4. Static analysis
Instruction frequencies
    Roughly 30% of all instructions are NOPs
27.06.2024

## Slide 35: 4. Static analysis
Instruction frequencies
  Roughly 30% of all instructions are NOPs
Instruction parallelism
  Average of 2.3 IPC (instructions per cycle)
27.06.2024

## Slide 36: 4. Static analysis
Instruction frequencies
  Roughly 30% of all instructions are NOPs
Instruction parallelism
  Average of 2.3 IPC (instructions per cycle)
  Conclusion:
  General-purpose code is not highly parallel
27.06.2024

## Slide 37: 5. Hardware complexity comparative analysis
Creating hardware floorplans
09-10-2020

## Slide 38: 5. Hardware complexity comparative analysis
Creating hardware floorplans
09-10-2020

## Slide 39: 5. Hardware complexity comparative analysis
Deriving hardware floorplans
Existing floorplans
27.06.2024

## Slide 40: 5. Hardware complexity comparative analysis
Deriving hardware floorplans
Existing floorplans
Block diagrams
27.06.2024

## Slide 41: 5. Hardware complexity comparative analysis
Deriving hardware floorplans
Existing floorplans
Block diagrams
Specifications datasheets
27.06.2024

## Slide 42: 5. Hardware complexity comparative analysis
Deriving hardware floorplans
Existing floorplans
Block diagrams
Specifications datasheets
Comparative analysis of four floorplans
09-10-2020
Intel P5 (Pentium) Intel P6 (Pentium II)
Intel Merced (Itanium) Intel Madison (Itanium 2)

## Slide 43: 5. Hardware complexity comparative analysis
Deriving hardware floorplans
Existing floorplans
Block diagrams
Specifications datasheets
Comparative analysis of four floorplans
Out-of-order complexity is similar to IA-64 scoreboarding
09-10-2020
Intel P5 (Pentium) Intel P6 (Pentium II)
Intel Merced (Itanium) Intel Madison (Itanium 2)

## Slide 44: 5. Hardware complexity comparative analysis
Deriving hardware floorplans
Existing floorplans
Block diagrams
Specifications datasheets
Comparative analysis of four floorplans
Out-of-order complexity is similar to IA-64 scoreboarding
Conclusion
Itanium’s EPIC only has – at best – marginal hardware improvements
09-10-2020
Intel P5 (Pentium) Intel P6 (Pentium II)
Intel Merced (Itanium) Intel Madison (Itanium 2)

## Slide 45: 6. Differentiation strategic framework
Marketing based on differentiation
27.06.2024

## Slide 46: 6. Differentiation strategic framework
Marketing based on differentiation
Target audience
    A b
Compare with competition
Update based on feedback
27.06.2024

## Slide 47: 6. Differentiation strategic framework
Marketing based on differentiation
Target audience
  Either general purpose (replace x86) or data center
Compare with competition
Update based on feedback
Datacenter Needs 2001 |  |  | 
64-bit |  |  | 
High performance |  |  | 
Energy efficiency |  |  | 
Cost-effectiveness |  |  | 
Compatibility with existing software |  |  | 
Security features |  |  | 
High reliability (RAS) |  |  | 
Multi-processor scalability |  |  | 
Long-term support |  |  | 
27.06.2024

## Slide 48: 6. Differentiation strategic framework
Marketing based on differentiation
Target audience
  Either general purpose (replace x86) or data center
Compare with competition
  What differentiates Itanium?
Update based on feedback
Datacenter Needs 2001 | Itanium | Intel x86 | AMD x86
64-bit | Yes | No | No
High performance | Med-High | High | Med-High
Energy efficiency | Low | Med | Med
Cost-effectiveness | Low | Med | High
Compatibility with existing software | No | Yes | Yes
Security features | Yes | No | No
High reliability (RAS) | Yes | No | No
Multi-processor scalability | Yes | No | No
Long-term support | Yes | Yes | Yes
27.06.2024

## Slide 49: 6. Differentiation strategic framework
Marketing based on differentiation
Target audience
  Either general purpose (replace x86) or data center
Compare with competition
  What differentiates Itanium?
Update based on feedback
  AMD64
Datacenter Needs 2003 | Itanium | Intel x86 | AMD x86
64-bit | Yes | No | Yes
High performance | Med | Med | High
Energy efficiency | Low | Med | Med
Cost-effectiveness | Low | Med | High
Compatibility with existing software | No | Yes | Yes
Security features | Yes | No | No
High reliability (RAS) | Yes | No | No
Multi-processor scalability | Yes | No | No
Long-term support | Yes | Yes | Yes
27.06.2024

## Slide 50: 6. Differentiation strategic framework
Marketing based on differentiation
Target audience
  Either general purpose (replace x86) or data center
Compare with competition
  What differentiates Itanium?
Update based on feedback
  AMD64
  Intel Xeon, and EM64T
Datacenter Needs 2004 | Itanium | Intel x86 | AMD x86
64-bit | Yes | Yes | Yes
High performance | Med | High | Med-high
Energy efficiency | Low | Med | Med
Cost-effectiveness | Low | Med | High
Compatibility with existing software | No | Yes | Yes
Security features | Yes | No | No
High reliability (RAS) | Yes | No | No
Multi-processor scalability | Yes | Yes | No
Long-term support | Yes | Yes | Yes
27.06.2024

## Slide 51: 6. Differentiation strategic framework
Marketing based on differentiation
Target audience
  Either general purpose (replace x86) or data center
Compare with competition
  What differentiates Itanium?
Update based on feedback
  AMD64
  Intel Xeon, and EM64T
  Normalizing of x86 extensions (XMP, RAS, SMX, etc.)
Datacenter Needs 2010 | Itanium | Intel x86 | AMD x86
64-bit | Yes | Yes | Yes
High performance | Med | High | Med-high
Energy efficiency | Low | Med | Med
Cost-effectiveness | Low | Med | High
Compatibility with existing software | No | Yes | Yes
Security features | Yes | Yes | Yes
High reliability (RAS) | Yes | Yes | Yes
Multi-processor scalability | Yes | Yes | Yes
Long-term support | Uncertainty! | Yes | Yes
27.06.2024

## Slide 52: 6. Differentiation strategic framework
Marketing based on differentiation
Target audience
  Either general purpose (replace x86) or data center
Compare with competition
  What differentiates Itanium?
Update based on feedback
  AMD64
  Intel Xeon, and EM64T
  Normalizing of x86 extensions
  Conclusion:
  It became challenging to market
27.06.2024
Datacenter Needs 2010 | Itanium | Intel x86 | AMD x86
64-bit | Yes | Yes | Yes
High performance | Med | High | Med-high
Energy efficiency | Low | Med | Med
Cost-effectiveness | Low | Med | High
Compatibility with existing software | No | Yes | Yes
Security features | Yes | Yes | Yes
High reliability (RAS) | Yes | Yes | Yes
Multi-processor scalability | Yes | Yes | Yes
Long-term support | Uncertainty! | Yes | Yes

## Slide 53: Summary
Explorative study to find the key reason why Itanium failed
Automated sentiment analysis
  Popular until ~2004
SPEC performance comparative analysis
  Comparable (sometimes better, sometimes worse)
Theoretical performance comparative analysis
  Case study of limitation of EPIC compared to traditional systems
Static analysis of IA-64 binaries
  Not much ILP to extract from software at compile-time
Hardware analysis
  x86 hardware is not much more complex than Itanium
Differentiation business strategy framework
  Itanium lost its competitive edge over x86 due to rapid developments from AMD and Intel
09-10-2020
MSc thesis: Why did Itanium fail?

## Slide 54: Conclusion
09-10-2020
MSc thesis: Why did Itanium fail?
Itanium was supposed to bring 64-bit, ILP and data center features, but the existing x86-family was eventually able to achieve all of these, so the extra investment was not well motivated.

## Slide 55: Discussion
09-10-2020
MSc thesis: Why did Itanium fail?
Broader implication of this conclusion
Cautionary tale for innovation companies/projects
How could Itanium have succeeded?
If AMD64 was never introduced
More feedback cycles from real-world implementations (instead of lab-tests)
More focus on OoO in hardware to benefit from dynamic optimizations
  Defeats the purpose of EPIC, but could save the project to bring the same competitive performance
Find or create niche market to build ecosystem

## Slide 56: Thank you for your attention
Kamron Geijsen